## Slide 1
OFF-GRID COMMUNICATION
Meshtastic, Meshcore,
And Mesh Radio
Open-source LoRa mesh networking for areas without infrastructure
By: N1TXN

## Slide 2
OVERVIEW
What We'll Cover
01
Mesh Networking & Meshtastic
Foundations, how it works
02
Hardware & Devices
Heltec, T-Deck, RAK, T-Beam and the ecosystem
03
Integrations: ATAK & MQTT
Tactical awareness plugins and internet bridging
04
Meshtastic vs MeshCore
Routing philosophies and when to choose each
05
Licensed vs Unlicensed
Ham radio rules versus ISM-band operation
06
Use Cases, Trade-offs & Getting Started
Applications, strengths, and next steps
MESHTASTIC | Off-Grid Mesh Communication
2

## Slide 3
FOUNDATIONS
What is Mesh Radio?
A mesh network is a decentralized topology where every node can relay data for others. Messages "hop" from device to device until they reach their destination — no central tower or internet required.
Self-Healing
If one node drops out, traffic automatically finds another path.
Infrastructure-Free
Works in remote areas, disasters, or anywhere cellular is unavailable.
Scalable Coverage
Each additional node extends the network. Range multiplies with hops.
MESHTASTIC | Off-Grid Mesh Communication
3

## Slide 4
COMPARISON
Meshtastic vs MeshCore
Same LoRa hardware, different philosophies. Not interoperable.
Dimension
Meshtastic
MeshCore
Routing
Managed flooding — any node can relay
Source routing — only Repeaters relay
Max Hops
Default 3, hard ceiling 7
Up to 64 hops
Client Role
Clients relay by default
Companions never relay
Scalability
Best for ad-hoc / mobile groups
Better for dense / planned nets
Handheld Battery
Good
Better (no relay duty)
Community
Large, global, mature
Smaller, growing (EU strong)
License / Cost
Fully open-source (GPL), free
MIT firmware; some app features paid
Best For
Hiking, events, zero-config use
Fixed repeaters, city/region meshes
MESHTASTIC | Off-Grid Mesh Communication
10

## Slide 5
THE PLATFORM
What is Meshtastic?
An open-source project that turns inexpensive LoRa radios into a long-range, off-grid communication platform.
LoRa-based
Unlicensed ISM bands (915 MHz US, 868 MHz EU). No ham license required for most use.
Long Range
Typical 1.25–3 mi; record of 205 mi under ideal conditions.
Decentralized
No dedicated router. Every node can send, receive, and relay.
Low Power
Days of battery life; solar-ready for fixed nodes.
Encrypted
AES-256 channel encryption. Private channels with shared keys.
App Connected
Pair via Bluetooth, Wi-Fi, or USB. Android, iOS, desktop.
MESHTASTIC | Off-Grid Mesh Communication
4

## Slide 6
TECHNICAL OVERVIEW
How Meshtastic Works
1
Send
App relays message to radio via Bluetooth, Wi-Fi, or serial.
2
Broadcast
Radio transmits LoRa packet. Retries up to 3× if needed.
3
Relay
Nodes check if seen before; if new, decrement hop & rebroadcast.
4
Deliver
Destination receives message. Nodes store ~30 packets offline.
Managed Flooding
A node listens briefly before rebroadcasting. If another node has already relayed the packet, it stays silent. This reduces congestion while ensuring robust multi-hop delivery. Default hop limit is 3 (up to 7).
MESHTASTIC | Off-Grid Mesh Communication
5

## Slide 7
TECHNICAL OVERVIEW
Packet Flow — Visual
Phone App
NODE A
Sender
Hops = 3
NODE B
Possible
Relay
NODE C
Possible
Relay
NODE D
Destination
App
Managed Flooding
Nodes listen briefly. If another node already rebroadcast, they stay silent — less airtime.
Hop Limit
Each rebroadcast decrements the hop counter. At 0 the packet stops — default max is 3.
MESHTASTIC | Off-Grid Mesh Communication
6
900mHz
900mHz
900mHz
Bluetooth
Bluetooth

## Slide 8
HARDWARE
Common Meshtastic Devices
Heltec V3/V4
Budget entry
ESP32-S3 + SX1262
OLED · ~$20–30
LILYGO T-Deck
Standalone unit
Screen + keyboard
No phone needed
RAK WisBlock
Modular & solar-ready
nRF52 + SX1262
Best for repeaters
LILYGO T-Beam
GPS tracker
ESP32 + SX1262
18650 battery slot
MESHTASTIC | Off-Grid Mesh Communication
7

## Slide 9
INTEGRATIONS
ATAK / TAK Plugin
Meshtastic bridges tactical team awareness off-grid via the official ATAK plugin and TAK module.
Position Sharing (PLI)
Real-time location of team members appears on the ATAK map over the mesh — no cell or internet.
GeoChat Bridging
Chat messages and CoT(cursor on target) events flow between ATAK and the Meshtastic mesh network.
TAK / TAK_TRACKER Roles
Set device role to TAK (or TAK_TRACKER for GPS-only nodes) for optimized CoT packets.
Server Relay & Packages
Optional relay of CoT to TAK servers; mission packages can transfer over Short/Turbo.
Setup: Install Meshtastic Android app + matching ATAK plugin APK → set device role to TAK → keep Meshtastic app running in background → green icon in ATAK confirms link. Standalone BLE plugin also available.
MESHTASTIC | Off-Grid Mesh Communication
8

## Slide 10
INTEGRATIONS
MQTT — Bridging Mesh to the Internet
MQTT lets an internet-connected gateway node forward mesh traffic to a broker, linking distant meshes and enabling maps, monitoring, and automation.
Local Mesh
LoRa nodes talk
over radio
Gateway Node
Wi-Fi / Ethernet
or phone proxy
MQTT Broker
mqtt.meshtastic.org
or private broker
Remote Mesh
Other gateways
inject traffic
Uplink / Downlink
Per-channel: uplink sends mesh → broker; downlink injects broker → mesh. Both optional.
Public Map & Monitoring
Position reporting feeds public maps. Integrate with Home Assistant, Node-RED, dashboards.
Privacy Controls
Encryption optional on MQTT path. Disable uplink on private channels. Client proxy via phone.
MESHTASTIC | Off-Grid Mesh Communication
9

## Slide 11
REGULATORY DETAIL
Licensed Ham vs Unlicensed (ISM)
Meshtastic supports both modes. Choice affects power, encryption, identification, and legal rules.
Unlicensed (ISM / Part 15)
Access & Rules
• No license, exam, or registration required
• Anyone can buy hardware and operate
• Must accept interference; no exclusive rights
Power & Spectrum
• US 915 MHz: max ~1 W EIRP (+30 dBm)
• EU 868 MHz: typically 25 mW + duty-cycle limits
• ISM bands only (no amateur allocations)
Encryption & Privacy
• Full AES-256 channel encryption allowed
• Private channels with shared keys supported
Licensed Amateur (Part 97)
Access & Identification
• Requires valid amateur radio license
• Must identify with callsign (long name)
• Subject to amateur band plans & rules
Power & Spectrum
• Higher power allowed (class & band dependent)
• Can use amateur allocations (e.g. 70 cm)
• Power limits lifted when is_licensed = true
Encryption Restriction
• Encryption generally prohibited under Part 97
• Meshtastic Ham Mode disables crypto automatically
MESHTASTIC | Off-Grid Mesh Communication
11

## Slide 12
CAPABILITIES
Key Features
Text Messaging
Group channels and direct messages across the mesh
GPS Location
Optional position sharing and node mapping
AES-256 Encryption
Channel-level encryption with shared keys
Excellent Battery Life
Days of operation; solar options for fixed nodes
Device Roles
Client, Router, Repeater, Tracker, TAK…
MQTT Bridge
Internet gateway for remote mesh access
MESHTASTIC | Off-Grid Mesh Communication
12

## Slide 13
APPLICATIONS
Real-World Use Cases
Outdoor & Adventure
Hiking, backpacking, skiing — stay in touch when cell disappears.
Community Mesh
Neighborhood or event meshes for private off-grid chat.
Emergency Prep
Disaster response and grid-down coordination.
IoT & Sensors
Telemetry and asset tracking over long distances.
Remote Infrastructure
Solar-powered fixed nodes for persistent coverage.
Education
Learn radio, networking, and embedded systems.
MESHTASTIC | Off-Grid Mesh Communication
13

## Slide 14
TRADE-OFFS
Advantages & Considerations
Strengths
▸ No infrastructure or fees
▸ Works when cellular is down
▸ Very low cost of entry
▸ Open-source & community-driven
▸ Strong encryption (unlicensed)
▸ Long range with multi-hop
▸ ATAK & MQTT integrations
▸ Excellent battery efficiency
Limitations
▸ Low bandwidth (text / small data)
▸ Not real-time voice or video
▸ Range depends on terrain
▸ Congestion in dense meshes
▸ Learning curve for advanced config
▸ Regulatory power/duty limits
▸ Not compatible with MeshCore
▸ Ham mode disables encryption
MESHTASTIC | Off-Grid Mesh Communication
14

## Slide 15
NEXT STEPS
Getting Started
1
Choose Hardware
Heltec, T-Deck, RAK, T-Beam… Prefer SX126x radios.
2
Flash Firmware
Web flasher. Set region. Choose Meshtastic or MeshCore.
3
Install App
Android / iOS Meshtastic app. Desktop CLI available.
4
Configure
Pair BT. Create channel. Set role (incl. TAK). Enable MQTT if desired.
5
Join / Integrate
Message the mesh. Optionally install ATAK plugin or MQTT gateway.
MESHTASTIC | Off-Grid Mesh Communication
15

## Slide 16
Resources & Community
Meshtastic
meshtastic.org
Docs · Discord · GitHub
ATAK Plugin · MQTT guide
MeshCore
meshcore.co.uk
Docs · Community maps
Web flasher available
Same hardware can run either firmware. ATAK and MQTT extend Meshtastic for tactical and internet use.
Build resilient, infrastructure-free communication — one node at a time.